## Slide 1
A Two-Channel Carry-Chain Time-to-Digital
Converter (TDC)
INTERNSHIP
Girdhari Jakhar
Entry no.: 2023EEB1201
Supervisor : Dr Devarshi Mrinal Das, Assistant Professor,
Dept. EE, IIT Ropar
Mentor: Azhar Yaseen N.J. , Researcher, ISDL, IIT Ropar
Krishan Mehra , Researcher, ISDL, IIT Ropar

## Slide 2
The Problem
2
A TDC answers one question: at what instant did an electrical event arrive?
Simplest method: count clock cycles. On a 200 MHz clock that is only 5 ns resolution.
5 ns of timing uncertainty = 75 cm of distance in LiDAR. Useless.
Applications like LiDAR, PET scanners and particle detectors need picoseconds — about 300x finer.
You cannot just run a faster clock: a 200 GHz clock does not exist on an FPGA.
The idea instead: measure the leftover time between the event and the next clock edge.
That leftover fraction is exactly what a fine "interpolator" recovers.

## Slide 3
The Solution: Coarse + Fine
3
COARSE — count clock edges (5 ns steps)
0
5 ns
10 ns
event
zoom in
FINE — carry chain subdivides the gap (~16 ps steps)
event lands here -> fine = number of taps
5 ns resolution (75 cm) -> 16 ps resolution (2.4 mm) = 312x finer
COARSE tells you which 5 ns cycle; FINE tells you where inside it.
The chain is 352 taps (5.63 ns) — a bit longer than a clock period, so nothing runs off the end.

## Slide 4
The Carry Chain as a Ruler
4
frozen on the clock edge
event
enters
1 1 1 1 1 1 1 1 1 0 0 0 0 0
edge reached this far
count the ones = 9 -> 9 x 16 ps = fine time
Real chains give a few "bubbles" (a stray 0 or 1); a 5-tap majority filter cleans them.
A validator flags any illegal code, so a corrupted shot is thrown away, not published.
The whole 352-bit code is turned into a number by a pipelined adder tree in ~5 ns.

## Slide 5
Reconstructing the Time
5
t_event = coarse x 5.000 ns - fine x tau
The event launches the chain; the clock freezes it.
So the fine value counts backwards from the clock edge — note the MINUS sign.
A larger fine value means the event arrived earlier (it had more time to climb).
Getting this sign backwards is a classic, silent error.
tau is the per-tap delay (~16 ps); coarse x 5 ns locates the clock edge itself.
The two chains have different tau, so the host applies a separate calibration per channel.

## Slide 6
Two Channels Make an Interval
6
one shared free-running counter
START (A)
STOP (B)
interval = t_STOP - t_START
One shared counter: its arbitrary start value cancels when you subtract the two timestamps.
Only the phase difference between the two events survives — that is the interval.
The counter is never reset, so a measurement never disturbs the timeline.

## Slide 7
Capturing at the Right Instant
7
The first clock edge after the event is the "golden edge" — the only instant that matters.
But the capture decision takes 4 clock edges (2-flop CDC sync + edge detect + FSM step).
By then the carry chain has saturated — it fills in about 5.6 ns.
First bring-up bug: this made fine read 255 on every single measurement.
Fix: snapshot_pipeline records the taps every edge and reaches back to the golden edge.
It keeps a 4-deep history, so the golden-edge snapshot is always still available.
CAPTURE_LAG = 4 is uniquely correct: 2-3 read a full chain, 5 reads an empty one.

## Slide 8
The Whole Signal Path
9
EVENT
CARRY
CHAIN
SNAPSHOT
BUBBLE
FIX
ENCODE +
VALIDATE
one channel — two identical copies (A = START, B = STOP)
x2 channels
INTERVAL
CALC
UART
HOST
(read_tdc.py)
No time is computed on-chip: tau_A != tau_B
and the bins are non-uniform, so the host
holds the per-channel calibration table.
interval = d_coarse x 5.000 ns - ( fine_b tau - fine_a tau )

## Slide 9
Engineering Problems Solved
10
Synthesis tried to delete the delay line -> DONT_TOUCH.
Async event caused intermittent missed captures -> two-flop CDC synchronisers.
Fine-encode path was 8x over the clock budget -> pipelined adder / reduction trees.
fine = 255 on every shot -> snapshot_pipeline (capture-lag fix).
Chain too short (18% dead zone) -> 64 -> 88 CARRY4 (352 taps).
Coarse and fine share one snapshot module, so they always describe the same clock edge.
Every fix was proven bit-identical to its predecessor against thousands of random vectors.

## Slide 10
Verification
11
554 automated checks — zero failures.
Five tiers: behavioural, synthesis, implementation (STA), timing simulation, hardware.
Each tier catches a class of bug the tier below structurally cannot.
Only Static Timing Analysis asks: does this path settle within one clock period?
Behavioural simulation can never prove clock-domain-crossing correctness.
A custom carry4_real model reproduces the measured bubbles and zero-width bins.
Encoder and validator were checked bit-identical to a reference at 256 and 352 taps.

## Slide 11
Implementation Results
12
CARRY4 = 249 — both delay lines survived optimisation.
SRL16E = 2 — all 704 tap registers are real flip-flops, not LUTs.
About 8% of the device used — room for a 4- or 8-channel instrument.
Timing closed: WNS = +0.318 ns at 200 MHz, zero failing endpoints.
Hold slack WHS = +0.084 ns, so there are no hold violations either.
Zero BRAM and zero DSP — the whole instrument is LUTs, flip-flops and carry logic.

## Slide 12
Hardware Experiment: Same Signal, Both Channels
13
No external time reference yet, so we first test the instrument on itself.
The same physical edge drives BOTH the START and the STOP channel.
The true interval is therefore a known constant (zero + fixed channel skew).
With a constant input, all scatter in the output is the instrument's own noise.
This is the only test that cleanly separates precision from accuracy.
A button press even works as a random-phase generator — a finger cannot control 5 ns timing.
The mean of the readings is the fixed skew; the spread is the single-shot precision.

## Slide 13
The Test We Ran
14
one
signal
START (A)
STOP (B)
Two-channel
TDC
reads 293 ps +/- 40 ps
293 ps is the fixed skew between the two channels — the instrument's zero point.
The input is constant, so the mean is the skew and the spread is the precision.
It is the only test that separates precision from accuracy without a reference.

## Slide 14
Hardware Results
15
Shots (two runs pooled) 622
Mean interval (channel skew) 293 ps
Single-shot precision (diff) 40.2 ps
Per channel (~ sigma / sqrt 2) ~28.5 ps (~4.3 mm LiDAR)
Run-to-run reproducibility < 1 ps
Measured on the 8-bit bring-up build; boundary wraps recovered in software.
This establishes precision — accuracy still needs a known reference.
Per-channel ~28.5 ps is about 4.3 mm of LiDAR round-trip per single shot.
Two independent runs agreed to under 1 ps, so the result is reproducible(it can be achieved from taking a , large number of samples , temp calibration voltage calibration )

## Slide 15
What the Spread Looks Like
16
213
253
293
333
373
interval (ps)
mean = 293 ps
sigma = 40 ps = single-shot precision
622 shots of the SAME interval — a tight cluster. The width IS the precision.
About 6% of raw shots wrapped at a clock-edge boundary and were recovered in software.
A calibrated build and averaging over many shots will tighten this spread further.

## Slide 16
What the Numbers Mean
17
Resolution (LSB, 16 ps): the finest step the ruler can mark — 2.4 mm.
Precision (~28.5 ps/channel): how repeatably it reads the same input — 4.3 mm/shot.
Accuracy: whether the reading equals the true value — not yet measured.
The 293 ps mean is a fixed skew (the zero point), calibrated out — not an error.
Precision (~28.5 ps) is roughly 1.8 LSBs — noise smears one reading across about two bins.
Averaging many shots tightens the estimate (by the square root of the count).

## Slide 17
Resolution / Precision / Accuracy
18
PRECISION
MEASURED
readings agree (28.5 ps)
293 ps skew
ACCURACY
NOT YET TESTED
needs a known-delay reference
The cluster is tight (precise) but offset — that offset is the 293 ps skew, calibrated out.
Resolution is the 16 ps grid; precision is about two grid steps (~1.8 LSB).
Accuracy needs a cable-loopback test against a known delay difference.

## Slide 18
Status & Remaining Work
19
Done: full two-channel datapath, timing closed, 554 checks, first hardware precision.
Next: floorplan the carry chains (pblock), for reproducible bin widths.
Next: code-density calibration -> per-bin LUT, DNL and INL.
Next: cable-loopback test -> verified accuracy against a known delay.
Next : use something faster than UART (currently we can only take around 1900 sample per clk cycle.
Next: Implement Temperature-Aware Calibration using the Spartan-7 XADC with temperature- dependent calibration LUT selection.
Next: Integrate Time Walk Compensation.

## Slide 19
Summary
20
~16 ps resolution on a clock that ticks every 5000 ps — a 312x improvement.
2.4 mm LiDAR distance resolution instead of 75 cm.
First hardware: ~28.5 ps per-channel single-shot precision, reproducible.
The hard part is everything around the delay line, not the delay line itself.
Six real bugs — deletion, CDC loss, timing, capture-lag, SRL, short chain — each diagnosed and fixed.
The design uses ~8% of the device, leaving headroom for a multi-channel instrument.

## Slide 20
[1] C. Favi and E. Charbon, "A 17ps Time-to-Digital Converter Implemented in 65nm FPGA Technology," ACM/SIGDA Int. Symp. on FPGAs (FPGA'09), 2009.
[2] Rui Machado , Jorge Cabral, and Filipe Serra Alves, “Recent Developments and Challenges in FPGA-Based Time-to-Digital Converters” IEEE TRANSACTIONS ON INSTRUMENTATION AND MEASUREMENT, VOL. 68, NO. 11, NOVEMBER 2019
[3] Y. Wang et al., "A Multi-Chain Merged Tapped Delay Line for High Precision Time-to-Digital Converters in FPGAs," IEEE Trans. Circuits Syst. II, vol. 65, no. 1, Jan. 2018.
[4] Ruqing Liu, Feng Li, Jingguo Zhu, Yan Jiang, Chenghao Jiang, and Tao Hu, “A High-Resolution Calibration Method for Time-to-Digital Converter of Lidar” Chinese Journal of Electronics vol. 34, no. 1, pp. 222–228, January 2025
[5] DONG Lei, YANGJun-Feng and SONG Ke-Zhui, “Carry-chain propagation delay impacts on resolution of FPGA-based TDC” NUCLEAR SCIENCE AND TECHNIQUES 25,030401(2014)
Reference